## Slide 1: Tiny Defect Detection for PCBs
ECE 5831 Pattern Recognition and Neural Networks
Group Members:
Rishikesh Dewalkar
Nikhil Pawar
Saurabh Raokhande
Notes: Divider Slide Option #2

## Slide 2: AGENDA
Group members and responsibilities
Introduction
Problem Statement
Objective
Techniques Used
Dataset
Model Architecture
Implementation
Results
Conclusion

## Slide 3: Group Members and Responsibilities
Rishikesh Dewalkar: Data collection, preprocessing, and annotation of PCB images with XML files.
Nikhil Pawar: Developed and trained the YOLOV8, focusing on real-time detection and performance evaluation.
Saurabh Raokhande: Developed and trained the Faster RCNN model, focusing on fault detection accuracy and model refinement.
Notes: Copy Slide Option #3

## Slide 4: INTRODUCTION
Importance of PCBs: PCBs are essential in modern electronics, providing electrical connections and mechanical support. Fault detection ensures reliability and performance.
Challenges in Traditional Methods: Manual inspections are slow, error-prone, and unsuitable for complex PCB designs. Rule–based algorithms struggle with variations in lighting and designs.
Advancements in Technology: Deep learning and computer vision automate fault detection, offering accuracy, scalability, and adaptability to manufacturing needs.
Our Contribution: Developed an automated system combining YOLOV8 for real-time detection and faster R-CNN for high-accuracy fault classification, addressing six common PCB defect types.

## Slide 5: PROBLEM STATEMENT
Challenges in Manual PCB Fault Detection:
Time-Consuming: Inspecting PCBs for fault is slow and labor-intensive, especially in large-scale manufacturing environments.
Human Error: Inspecting PCBs by hand increases the likelihood of missing defects or making incorrect assessments, leading to faulty products passing through quality control.
Complexity of Faults: Some PCB faults can be subtle and difficult to detect, such as tiny spur traces or open circuit that might not be easily visible.

## Slide 6: OBJECTIVE
Automate Fault Detection in PCBs: Develop an automated system to accurately detect and classify common PCB faults (mouse bite, missing hole, open circuit, short, spur, and spurious copper) using deep learning models.
Improve Manufacturing Efficiency: Reduce the time and labor involved in manual inspection by implementing a real-time fault detection system that works efficiently in a production line.
Enhance Detection Accuracy: Achieve high detection accuracy for all six PCB fault types, minimizing the risk of defective boards being passed in quality control.
Enable Scalable and Cost-Effective Quality Control: Design a system that can scale to handle large quantities of PCBs, reducing overall production costs and improving the consistency of the manufacturing process.

## Slide 7: TECHNIQUE USED
YOLO v8 (You Only Look Once version 8)
Real-Time Detection: YOLO v8 enables fast, real-time object detection, which is ideal for quick quality control in PCB production.
Efficiency and Speed: It processes images in one pass, making it highly efficient for detecting multiple faults simultaneously.
Faster RCNN ResNet (Region-based Convolutional Neural Network with ResNet Backbone)
High Accuracy: Faster RCNN with ResNet excels at detecting subtle and complex faults, ensuring precise detection.
Robust Feature Extraction: ResNet enhances the model’s ability to identify faults across different scales and orientations.

## Slide 8: DATASET
Images and XML Files: The dataset consists of PCB images paired with XML files containing annotations (bounding boxes and labels).
Fault Types: The dataset includes six PCB defects: mouse bite, missing hole, open circuit, short circuit, spur, and spurious copper.
Annotations: XML files contain bounding box coordinates and class labels for each fault, guiding the model’s learning.
Preprocessing: Images are resized, normalized, and augmented (e.g., rotation, flipping) to improve model robustness and generalization.

## Slide 9: IMPLEMENTATION DETAILS
Environment Setup: The project uses Python with PyTorch for model development and OpenCV for image preprocessing. GPU acceleration is utilized for faster training.
Data Preprocessing: Images are resized, normalized, and augmented (via rotation, flipping, scaling) to prepare the dataset for training and improve model robustness.
Model Training: The dataset is split into training (80%) and validation (20%) sets. Adam optimizer and appropriate loss functions (e.g., classification, bounding box loss) are used for training.
Evaluation and Inference: The model’s performance is evaluated using mAP and IoU metrics. During inference, Non-Maximum Suppression (NMS) is applied to remove overlapping predictions.

## Slide 10: Faster RCNN Demonstration

## Slide 11: Faster RCNN Model Architecture
min_loss = sys.maxsize num_epochs = 25 model=load_model().to(device) models.append(model) params = [p for p in model.parameters() if p.requires_grad] optimizer = torch.optim.Adam(params, lr=0.0001, weight_decay=0.0005,) lr_scheduler = torch.optim.lr_scheduler.StepLR(optimizer, step_size=3, gamma=0.1) loss_curve=[] IOU_curve=[]

## Slide 12: YOLOV8 Demonstration

## Slide 13: YOLOV8 Model Architecture
Input Layer:
  Resizes images to imgsz=640 and normalizes inputs.
Backbone and Neck:
  Backbone: CSPDarknet53 extracts features using convolutional layers and CSP modules.
  Neck: PANet performs multi-scale feature fusion with upsampling and concatenation.
Head and Post-Processing:
  Head: Anchor-free design predicts classes, bounding boxes, and objectness scores.
  Post-Processing: Non-Maximum Suppression (NMS) filters overlapping predictions.
Key Hyperparameters:
  Batch: 16 | Epochs: 100 | Learning Rate: lr0=0.001, lrf=0.0001
  Image Size: 640 | Mixup: 0.3 for data augmentation.

## Slide 14: RESULTS
YOLOV8 Predictions
Faster RCNN Predictions

## Slide 15: FUTURE WORK
Hybrid Model Exploration: Investigate combining YOLO v8 and Faster RCNN for better speed and accuracy.
Dataset Expansion: Add more fault types and PCB variations for improved generalization.
Model Optimization: Implement pruning or quantization for faster inference.
Automated Annotation: Develop tools for faster, scalable PCB fault image annotation.

## Slide 16: Thank You